## Slide 1: FilmStar 二次开发用户需求 (102521)
老鹰半导体

## Slide 2: Python Programing Next Step
Design wavelength:
  Our default value = 940nm
  850nm was added back in April
  Now we need to add 905nm
F, B and T design generation: A new situation of multiple {QW} structures
N and P profile: a default value of 1e17 is to be assigned when it’s left ‘blank’
Summary Data Table: all data to be normalized and combined to together into one single data file template

## Slide 3: 1. Design wavelength
Dataprocessing.py is supposed to get input design wavelength. For example, we need 905nm this time

## Slide 4: F, B and T design generation: A new situation of multiple {QW} structures
B Design
Our new design will have multiple {QWs}.
The F and B designs stay unchanged.
But we need a new algorism to generate the T (top) designs as shown above
T design
B Design
T design
New FBT
Design Generation
B design 从上到下遇到第一个QW 包括QW以下全部删除 现在B design不改变
以前T design 遇见QW以上全部删除 下面保留并反转次序 现在 T design 需要找到从下到上遇到的第一个QW以上全部删除 下面保留并反转次序